## Slide 1
2.2 Methods of error detection
Automatic Repeat Query (ARQ)

## Slide 2
Error detection methods
Error detection methods
Parity block checks
Echo checks
Automatic Repeat Query (ARQ)
Parity checks
Checksums
Check digits

## Slide 3
Automatic Repeat Query (ARQ) is another method that can be used to verify that transmitted data has arrived unchanged – and thus, error-free.
ARQ is often used by mobile phone networks to ensure data integrity. It includes the following key features:
Automatic Repeat Query (ARQ)
Positive acknowledgements
Message sent to the sender indicating that data has been received correctly.
Negative acknowledgements
Message sent to the sender indicating that data has not been received correctly.
Timeout
The time allowed to elapse before an acknowledgment is received.

## Slide 4
The destination device receives the data transmission along with an error detection code, typically a Cyclic Redundancy Check or CRC – this is used to determine if the data contains any transmission errors.
Automatic Repeat Query (ARQ)
Destination
Sender
Data transmitted along with an error detection code

## Slide 5
If no errors have been detected, a positive acknowledgement is sent back.
Automatic Repeat Query (ARQ)
Destination
Positive acknowledgement
Error detected?
Sender

## Slide 6
If an error is detected, a re-transmission request is sent back to the sender.
The sender then re-transmits the original message.
Automatic Repeat Query (ARQ)
Destination
Negative acknowledgement
Error detected?
Data retransmitted along with an error detection code
Sender

## Slide 7
Automatic Repeat Query (ARQ)
Destination
Sender
Data transmitted along with an error detection code
The timeout is a feature used by the sending device. After a pre-determined amount of time, if the device hasn’t received any form of acknowledge, it will automatically re-send the data.
The device will keep re-sending the data until it either receives a positive acknowledgement or a pre-configured number of attempts to re-send the transmission have taken place.

## Slide 8
Automatic Repeat Query (ARQ) is a method which can be used to verify that transmitted data has arrived error free, often used by mobile phone networks to ensure data integrity. It works as follows:
  The destination device receives the data transmission along with an error detection code.
  The code is used to determine if the data contains any transmission errors.
  If no errors have been detected, a positive acknowledgement is sent back.
  If an error is detected, a re-transmission request is sent back to the sending device.
  After a pre-determined amount of time, if the sending device hasn’t received any form of acknowledge, it will automatically re-send the data.
  It will keep doing this until it either receives a positive acknowledgement or a pre-determined number of attempts to re-send the transmission have taken place.
Automatic Repeat Query (ARQ)