## Slide 1
3.1 Computer architecture
Von Neumann architecture

## Slide 2
Calculators are examples of computers – they take inputs, process them and output a result.
Fixed- and stored-program computers
John von Neumann designed computers with stored programs.

## Slide 3
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Key characteristics
  Central processing unit (CPU)
  Control unit (CU)
  Arithmetic logic unit (ALU)
  Cache
  Clock
Cache
Clock

## Slide 4
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Notice how both instruction data and program data are stored in the same memory in binary form.
Cache
Clock

## Slide 5
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Notice how both instruction data and program data are stored in the same memory in binary form.
Cache
Clock

## Slide 6
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Program counter (PC)
Holds the address of the next instruction to be executed in memory.
Cache
Clock

## Slide 7
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Memory address register (MAR)
Holds the memory address where data is to be fetched from or written to.
Cache
Clock

## Slide 8
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Memory data register (MDR)
Holds data fetched from or to be written to memory.
Cache
Clock

## Slide 9
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Accumulator
Holds the results of calculations.
Cache
Clock

## Slide 10
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Fetch
Decode
Execute
Cache
Clock
Fetch stage
The program counter is checked for the memory address of the next instruction to be executed.

## Slide 11
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Fetch
Decode
Execute
Cache
Clock
Fetch stage
The program counter is checked for the memory address of the next instruction to be executed.
The memory address register (MAR) fetches the instruction from main memory (RAM) and brings it into the memory data register (MDR).

## Slide 12
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Fetch
Decode
Execute
Fetch stage
The program counter is checked for the memory address of the next instruction to be executed.
The memory address register (MAR) fetches the instruction from main memory (RAM) and brings it into the memory data register (MDR).
The program counter is incremented so it points to the next instruction.
Cache
Clock

## Slide 13
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Fetch
Decode
Execute
Cache
Clock
Decode stage
Now the instruction is in the CPU, the control unit (CU) decodes it to figure out what the CPU needs to do.

## Slide 14
Von Neumann architecture
Central processing unit (CPU)
Control
unit (CU)
Arithmetic logic unit (ALU)
Register
Memory address register (MAR)
Memory data register (MDR)
Program counter (PC)
Accumulator
Main memory (RAM)
Address | Data
1 | Load address 5
2 | Add address 6
3 | Store in address 6
4 | End
5 | 23
6 | 12
Fetch
Decode
Execute
Cache
Clock
Execute stage
Now the CPU can execute the instruction. What it actually does depends on the instruction. It could be asked to:
  Go back to main memory (RAM), fetch data and add it to the accumulator.
  Jump to another instruction.
  Write data held in the accumulator back into main memory (RAM).

## Slide 15
The von Neumann architecture consists of a:
  Control unit (CU)
  Arithmetic logic unit (ALU)
  Main memory (RAM)
  Inputs and outputs
The von Neumann architecture is based on the stored program concept.
Both instruction data and program data are stored in the same memory in binary form. There is no way to know if the pure binary held in memory represents instructions or data simply by looking at it.
A von Neumann CPU contains the following registers:
  Program counter (PC): Holds the address of the next instruction to be executed in memory.
  Memory address register (MAR): Holds the memory address where data is to be fetched from or written to.
  Memory data register (MDR): Holds data fetched from or to be written to memory.
  Accumulator: Holds the results of calculations.
Von Neumann architecture